## Slide 1: TEAM J.O.Y. Design Review 1
Noah Judelson, Zack Wojtalik,
Kai Matthews, Cash Collum
Notes: Noah – 30 second intro

## Slide 2: Agenda
Our Design
Tools and Sizing Method Development
Sizing, Mission Analysis and Constraints
Structural, Stability, and Operational Considerations
Conclusions
Notes: Noah – 30 second intro

## Slide 3: Our Design Concept
Conventional Design
High Lift Device
  Blown Flaps
High Wing
Twin Propellor
Tail Dragger
Tail Dragger
Blown Flaps
Notes: Kai - 2 min

## Slide 4: Our Design & Mission Profile
Spec | Our Value
W0 | 49 lbs
We | 19 lbs
S | 11 ft2
b | 8 ft
AR | 6
 | 0
 | 0
Spec | Our Value
W0 | 49 lbs
We | 19 lbs
S | 11 ft2
b | 8 ft
AR | 6
 | 0
 | 0
Notes: Quick yap about the general dimensions of our aircraft and the mission profile – climb segments, top speed segment (150mph for 10min), 1 hour cruise segment, loiter and descent

## Slide 5: Tools and Sizing Method Development
Notes: Kai - 2 min

## Slide 6: Component Weight Model Modification
Light-Weight PLA structure
Bulkheads/Spars modeled separately
2x skin thickness sensitivity
Iterated W0 to converge
19 lb
31 lb
30 lb
Notes: Noah – 45 seconds
surface area × thickness estimates the material volume. Multiplying by density gives that part’s weight. The 1.05 is a 5% multiplier used in the code.
- Included skin thickness sensitivity study to show Raymer is definitely overestimating, and note that this estimates a 100% infill LWPLA
Noah – 45 seconds
𝑊_𝑖=1.05 𝜌_𝑖 𝑆_("wet" ,𝑖) 𝑡_𝑖
surface area × thickness estimates the material volume. Multiplying by density gives that part’s weight. The 1.05 is a 5% multiplier used in the code.
- Included skin thickness sensitivity study to show Raymer is definitely overestimating, and note that this estimates a 100% infill LWPLA

## Slide 7: Assumptions and Breakdown
Assumption | Value
LWPLA Density | 38 lb/ft3
LW Balsa Density | 5.5 lb/ft3
Wing Spar (Nested CF Pair) | 0.3 lb
Wing Skin Thickness | 0.2 in
Stabilizer/Fuse Skin Thickness | 0.1 in
100% PLA infill
Minimal wing support
LG/Actuator weight
Notes: Noah – 45 seconds
Spar info: 16/14mm & 14/12mm, 0.29 lbs per

## Slide 8: High Lift Devices
Plain
Split
Slotted
Flap Type |  | 
Plain | 0.9 | 0.3240
Split | 0.9 | 0.3240
Slotted | 1.3 | 0.4680
Flap Type |  | 
Plain | 0.9 | 0.3240
Split | 0.9 | 0.3240
Slotted | 1.3 | 0.4680
Raymer, D. P., Aircraft Design: A Conceptual Approach, 7th ed., AIAA Education Series, American Institute of Aeronautics and Astronautics, Reston, VA, 2024.
Notes: ZACK – 1.5 min
Raymer said to take 60-80% of these values
Can also implement leading edge slot – increases stall angle of attack and can be fixed
I have pdf of blown flap paper for prop planes, they used a 4" propeller on a 2D airfoil in a wind tunnel. Results show that more blowing will yield a higher sectional lift coefficient like we expected for a slotted flap design. With flap deflection we can achieve a conservative Cl estimate of 2 but potentially up to 4.
1.5 min

## Slide 9: Sizing, Mission Analysis and Constraints
Notes: Kai - 2 min

## Slide 10: Point Performance Evaluation
Mission Characteristics
150mph Max Speed for 10 minutes
1.5 hr flight time
Cruise @ 15,000ft
Notes: Zack - 1.5 min

## Slide 11: Wingspan and Root Chord Analysis
Original Values showed too much loading
Increase Planform Area and Aspect Ratio for better loading
Diminishing return and manufacturing concerns occur as wingspan increases
Notes: Cash - 1.5 min

## Slide 12: Structural, Stability, and Operational Considerations
Notes: Kai - 2 min

## Slide 13: Structural Considerations
Segmented LW-PLA construction
  Precise, replicable, size limited
  Plan to reinforce joints
High lift devices – plain blown flaps
  Complexity vs. Lift tradeoff
Spanwise wing spar system
  Wind gust G requirements
Fixed tailwheel landing gear
  Consider landing load distribution
Notes: Noah - 1.5 min
Segmented LW-PLA: Fits printer limits; reinforce joints to transfer loads.
Plain blown flaps: Simple mechanism; reinforce hinges and servo mounts.
Wing spar: Carries bending loads into fuselage; surrounding structure resists twisting.
Fixed tailwheel: Intended for larger-prop clearance; reinforced mounts carry landing loads without retraction hardware.

## Slide 14: Stability Considerations
High Wing for Inherent Roll Stability
Static Margin
RFP requires between 10-15% Static Margin
Analysis using baseline values shows roughly 8 different designs
                Battery in front, Payloads surrounding CG, and Electronics in the back gives 12-14% Static Margin throughout all stages
Notes: Cash - 1.5 min

## Slide 15: Operational Considerations
Design Choice | Operational Consideration
Tail Dragger | Unstable ground steering
Blown Flaps | Decreased Landing Speed + STOL
High Wings | Less maneuverability
Notes: Kai - 1.5 min – BE READY TO ANSWER QUESTIONS? TALK ABOUT THIS

## Slide 16: Conclusions
Notes: Kai - 2 min

## Slide 17: Conclusion
Why Team Joy?
Meets RFP requirements
Manufacturable design
Pilotable
Pros | Cons
High lift at low velocity | Unstable Ground Steering
Propellor clearance | Less ground maneuverability
High stability | 
Design Simplicity | 
Notes: Kai - 1.5 min

## Slide 18: Questions?

## Slide 19: Plan for the Future
Weight model accuracy improvements
Continue building analytical blown flap model
Trade study on
Wing internal structure design
Add anhedral for stability reduction

## Slide 20: Trade Tree

## Slide 21: BMF Variation Over Mission

## Slide 22: COTS Component Links
Motor: https://www.scorpionsystem.com/catalog/aeroplane/motors_1/sii-40/SII-4035-250/
Battery: https://store.foxtech.com/Diamond-pro-330wh-kg-solid-state-battery/
Actuator: https://www.hiteccs.com/actuators/product-details/D954SW
Landing Gear: https://whiteroseeng.com/products/tf.php
Wing Spar: https://www.readymaderc.com/products/details/86721-strix-nesting-pair-1m-3k-carbon-fiber-spar-tubes-16-14mm-14-12mm
Telemetry: https://holybro.com/products/sik-telemetry-radio-v3

## Slide 23: RFP Requirements Matrix
https://o365coloradoedu-my.sharepoint.com/:x:/r/personal/noju6274_colorado_edu/Documents/SeniorProj_RFPMatrix.xlsx?d=wcb930d652b0b4a6f84c19509cf3024b3&csf=1&web=1&e=EzohYa